## Slide 1: About Prefetch
YT
2018-6-11

## Slide 2
Agenda
What is prefetch?
How to metric prefetch?
Any hardware prefetch methods?
What major concerns of prefetch?
Which prefetch method to choose?

## Slide 3: What is prefetch?

## Slide 4
Get information before needed
Prefetch is used for cache, is one method to reduce cache miss penalty
It predicts which line will be needed and fetch them in advance
A prefetch algorithm must be carefully designed if the machine performance is to be improved rather degraded

## Slide 5: How to metric prefetch?

## Slide 6
Three important metrics
Coverage: indicates the fraction of memory requests that were supplied by the prefetcher rather than being demand-fetched
Accuracy: indicates the fraction of the prefetched cache lines offered to the processor that were actually used
Timeliness: indicates if the data offered by the prefetcher arrives before it is needed, but not so early that the data must be discarded before it be used

## Slide 7: Any hardware prefetch methods?

## Slide 8
OBL prefetcher(1/6)
[1982: Cache Memories, Alan Jay Smith]
[1990: Improving Direct-mapped Cache Performance by the Addition of a Small Fully-associative Cache and Prefetch buffer, Norman P. Jouppi]
If line i is referenced, only line i+1 is considered for prefetching
Upon referencing block i, the operations are: prefetch block i+1 unconditionally, only on a miss to block i, or if the prefetch has been successful in the past
OBL: One Block Look-ahead

## Slide 9
OBL prefetcher(2/6)
Infrastructure
OBL can successful for the optimization of ICache

## Slide 10
OBL prefetcher(3/6)
memory access model
Instruction execution occurs in a sequential fashion (unless explicitly modified) from one instruction to the next

## Slide 11
OBL prefetcher(4/6)
design goals
When a miss occurs, begin prefetching successive lines starting at the miss target and store in a stream buffer to avoid cache pollution

## Slide 12
OBL prefetcher(5/6)
Hardwar Structure
about 100B storage
StreamBuffer: 4-entry

## Slide 13
OBL prefetcher(6/6)
When a miss occurs, the stream buffer begins prefetching successive lines starting at the miss target. As each prefetch request is sent out, the tag for the address is entered into the tag field, and the valid bit is set to 0. When the prefetch data returns, the valid bit is set to 1.
Subsequent miss also compare their address against the first item stored in the buffer. If hit, the cache can be reloaded in a single cycle from stream buffer. If miss, flush stream buffer and restart at the new miss address.

## Slide 14
RPT prefetcher(1/6)
[1991: An Effective On-chip Preloading Scheme to Reduce Data Access Penalty, Jean-Loup Baer]
The RPT use the prediction of instruction stream and data access address to preload required data for DCache
Data with regular access patterns is preloaded, independently of the stride size, a preloading of data with irregular access patterns is prevented
RPT： Reference Prediction Table

## Slide 15
RPT prefetcher(2/6)
Infrastructure
Can see instruction PC
Can use physical or virtual address

## Slide 16
RPT prefetcher(3/6)
memory access model
Inner loop
m-nested loops memory access patterns can be divided into four category: scalar, zero stride, constant stride, irregular

## Slide 17
RPT prefetcher(4/6)
design goals
Generate preloads for uncached blocks in the scalar, zero stride, and constant stride access categories independently of the stride size.
At the same time, avoid unnecessary preloading for the irregular accesses

## Slide 18
RPT prefetcher(5/6)
Hardwar Structure
about 2KB storage
RPT: 256-entry

## Slide 19
RPT prefetcher(6/6)
load/store PC and EA update RPT: if PC miss, instruction is entered, the prev_addr is set to EA, stride to 0, and state to Init; if hit, write EA to pre_addr, and check stride correct to update state and stride
LA-PC reference RPT to generate prefetch by the state: if miss, no operation; if hit , a block address (prev_addr+stride) is compute, if the state is steady, the block is uncached, and the address not exist in request queue, a preload is initiated.
EA: Effective Address
LA-PC: Look-ahead PC, the prediction PC by BPT

## Slide 20
C/DC prefetcher(1/6)
[2004: AC/DC, An Adaptive Data Cache Prefetcher, Kyle J. Nesbit]
C/DC prefetching divides memory into fixed size zone. Then, it looks for delta patterns within each zone
To the basic GHB structure, we add a small delta buffer, a correlation key register, and a correlation comparison register
C/DC: CZone/Delta Correlation

## Slide 21
C/DC prefetcher(2/6)
Infrastructure
Can see L2 hit/miss
Use physical address

## Slide 22
C/DC prefetcher(3/6)
memory access model – delta pattern
( 8,32) > 24, 8, 32, 24 …
(32,24) > 8, 32, 24, 8 …
(24, 8) > 32, 24, 8, 32 …
In general, the sequences of deltas used for correlation can be any length. We undertook a preliminary study that indicated that pairs of delta are a good choice

## Slide 23
C/DC prefetcher(4/6)
design goals
Match current delta pair with history delta pair to find possible subsequent delta sequence

## Slide 24
C/DC prefetcher(5/6)
Hardwar Structure
Plus prefetch tag bit for every L2 Cache line total use about 2KB storage
IT: 256-entry
GHB: 256-entry

## Slide 25
C/DC prefetcher(6/6)
L2 miss or prefetch hit address is used to access IT, if hit, get a pointer to GHB miss address list in the same CZone
The address list are used to compute delta sequence. The first and second delta are shift to key register. The others are shift into correlation comparison register one by one
At each step the comparison register and the key register are compared. If the register match, a correlation has been detected and prefetching is trigged
As deltas are shifted to register, they are also shifted into the delta buffer, and used to generate prefetching addresses until prefetch degree

## Slide 26
AMPM prefetcher(1/9)
[2009, Access Map Pattern Matching Prefetch: Optimization Friendly Method, Yasuo Ishii]
The AMPM is a optimization-friendly prefetch method.
The AMPM prefetcher stores the 2-bit access states of all cache lines of hot zones in the memory access pattern maps. These access states in the map are stored without any access order.
AMPM: Access Map Pattern Matching

## Slide 27
AMPM prefetcher(2/9)
Infrastructure
Can see L2 hit/miss
Use virtual address

## Slide 28
AMPM prefetcher(3/9)
memory access model - cache line state
Cache line granularity memory access state static
Every cache line have four possible state, stored in a two-bit state machine

## Slide 29
AMPM prefetcher(4/9)
memory access model - zone
Memory space is divided into zone. “Hot zone” is detected on the basis of the recent zone access frequency
All cache lines 2-bit access sates of hot zone are stored in the memory access pattern maps.
The number of hot zones and memory access pattern maps is fixed, and they are stored in a memory access map table and replaced by the LRU policy

## Slide 30
AMPM prefetcher(5/9)
memory access model – access map pattern
-N == (Access|Success) && -2N ==(Access|Success) && +N==Init,
+N is a prefetch candidate
+N == (Access|Success) && +2N ==(Access|Success) && -N==Init,
-N is a prefetch candidate

## Slide 31
AMPM prefetcher(6/9)
design goals
Divided memory space into adaptive zone size
Record hot zone access map pattern, find the prefetch candidates by pattern matching
Adjust prefetch aggressiveness dynamically by monitor cache pollution and prefetch accuracy

## Slide 32
AMPM prefetcher(7/9)
Hardwar Structure
Total use 29439-bit storage
BPNum: Backward Prefetching Number; FPNum: Forward Prefetching Number

## Slide 33
AMPM prefetcher(8/9)
The AMPM prefetcher divides main memory space into fixed sized areas, and detects “hot zones” on the basis of the recent-zone-access frequency
It stores the 2-bit access states of all cache lines of hot zones in the memory access patterns maps. The number of hot zones and memory pattern maps is fixed, and they are stored in a memory access map table and replaced by the LRU policy

## Slide 34
AMPM prefetcher(9/9)
When memory access requests arrive, the AMPM prefetcher tries to detect the stride address correlation by pattern matching using the memory access pattern map and determines the prefetch candidates
It also decides which prefetch requests are appropriate and issues these requests to the main memory
It also decides the number of requests to issue on the basis of the profiled information

## Slide 35
BO prefetcher(1/8)
[2015, A Best Offset Prefetcher, Dierre Michaud]
The BO prefetcher submitted to the DPC2 contest prefetches one line into the L2 cache on every cache miss or hit on a prefetched line.
The BO prefetcher tries to find automatically an offset value that yields timely prefetches with the highest possible coverage and accuracy
BO: Best Offset
DPC2: The 2nd Data Prefetching Championship

## Slide 36
BO prefetcher(2/8)
Infrastructure
Can see L2 hit/miss
Use physical address
Can see MSHR occupancy
Restricted from crossing 4KB page boundary
MSHR: Miss Status Holding Register

## Slide 37
BO prefetcher(3/8)
memory access model - sequential stream
Offset can be 1 or multiple of 1
If the offset is too small, prefetches may not be timely

## Slide 38
BO prefetcher(4/8)
memory access model - stride stream
Constant byte stride leads periodic line strides 1, 2, 1, 2…
Offset can be 3 or multiple of 3
Offset prefetching can (in theory) deliver 100% coverage and accuracy on any periodic sequence of line strides, by setting the offset equal to the sum of the strides in a period, or equal to a multiple of that number.

## Slide 39
BO prefetcher(5/8)
memory access model - interleaved stream
Stream 1 alone can be prefetched perfectly with a multiple of 3 as offset. Stream 2 alone can be prefetched perfectly with a multiple of 2 as offset. Both streams can be prefetched perfectly with a multiple of 6 as offset

## Slide 40
BO prefetcher(6/8)
design goals
Find the unique suitable next phase offset by last phase learning
Adjust prefetch aggressiveness dynamically by monitor memory bandwidth
Turn off prefetcher when detected bad prefetch behavior

## Slide 41
BO prefetcher(7/8)
Hardware Structure
Total use 4361-bit storage
Offset ROM value: ±1,2,3,4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,20,24,30,32,40

## Slide 42
BO prefetcher(8/8)
When reset, phase prefetch offset O=1, all scores=0
On every L2 miss or prefetch hit of address X, prefetch X+O
Every X, put in delay queue, after fixed time, send to RR left table; Every prefetched line address Y, send Y-O to RR right table
Every X, test the nth offset On from the list by searching if the line address X-On is in the RR table. If hit, score for offset On is increased. The next L2 access tests offset On+1 and so on
Learning phase finishes after 100 rounds, or if one of the scores reaches 31. Selected the offset with the greatest score as next phase prefetch offset, scores and round counter are reset, a new phase starts

## Slide 43: What major concerns of prefetch?

## Slide 44
Three major concerns
When to initiate a prefetch?
Always, miss, prefetch hit
Which line(s) to prefetch?
Different pattern detect algorithm
Where to place fetched line(s)?
L1/L2 Cache, stream buffer

## Slide 45: Which prefetch method to choose?

## Slide 46
Existent problems
OBL: successful for optimization of instruction streams, but much less so for data streams.
RPT: PC-based RPT only suitable for DCache, not useful for L2 Cache. Because PC may be difficult or costly to obtain for L2 Cache implementation, and more important, L2 Cache suffer from L1 Cache screening.
C/DC: all GHB based prefetchers must rely on memory access order information, out-of-order memory access optimization may disturb such order.

## Slide 47
Add prefetcher for L2 Cache
Prefetching logic added to primary cache increase complexity and may increase processor cycle time
A larger L2 Cache can tolerate more cache pollution caused by prefetching than small primary cache
Modern out-of-order processors can tolerate most primary cache misses with relatively little performance degradation
Primary access stride can also be detected by good L2 Cache access pattern detect algorithm

## Slide 48: Bingo !!!