## Slide 1: About Rename
YT
2017-6-11

## Slide 2
Agenda
What is rename?
Why need to rename?
How to rename?
What other matter we need to deal?
Which method can we choose?

## Slide 3: What is rename?

## Slide 4
Change logic reg to phy reg
add $r3, $r2, $r1 #assembly instruction
add R3, R2, R1 #actual operation

## Slide 5: Why need to rename?

## Slide 6
Scalar Structure

## Slide 7
Data Hazard in Scalar
add $r3, $r2, $r1
add $r4, $r5, $r3 #hazard on $r3, RAW
add $r5, $r2, $r1
add $r5, $r6, $r7

## Slide 8
Superscalar Structure

## Slide 9
Superscalar Features
Parallel Pipeline: initial the processing of multiple instructions in every machine cycle
Diversified Pipeline: employing multiple and heterogeneous functional units
Dynamic Pipeline: instructions issue and execution out of order. Execution sequence is defined as the run-time checking for availability of data and resources, not as program order.

## Slide 10
Data Hazard in Superscalar
add $r3, $r2, $r1
add $r4, $r5, $r3 #hazard on $r3, RAW
add $r5, $r2, $r1 #hazard on $r5, WAR
add $r5, $r6, $r7 #hazard on $r5, WAW
More hazard occurs because of out of order execution!!!

## Slide 11: How to rename?

## Slide 12
Add time info for logic reg
When multiple instruction executing out of order, we need to know instructions use the same logic register which in front
The way we choose is to use different physical registers to represent the same logic register in different time
Then we need tables to record mappings from logic to physical and mappings from physical to logic

## Slide 13
Rename from logic to phy
add $r3, $r2, $r1
add $r4, $r5, $r3
add $r5, $r2, $r1
add $r5, $r6, $r7
add $r3, $r4, $r6
add $r5, $r3, $r1
add $r3, $r1, $r5
add $r2, $r3, $r1
add R32, R02, R01
add R33, R05, R32
add R34, R02, R01
add R35, R06, R07
add R36, R33, R06
add R37, R36, R01
add R38, R01, R37
add R39, R38, R01
rename

## Slide 14
Single PRF to rename(1/7)

## Slide 15
Single PRF to rename(2/7)
Use two instructions to explain renaming process
add $r2, $r1, $r1
add $r30, $r1, $r2

## Slide 16
Single PRF to rename(3/7)
Rename after instruction “add $r2, $r1, $r1”

## Slide 17
Single PRF to rename(4/7)
Rename after instruction “add $r2, $r1, $r1; add $r30, $r1, $r2”

## Slide 18
Single PRF to rename(5/7)
State after instruction “add $r2, $r1, $r1” execution finished

## Slide 19
Single PRF to rename(6/7)
State after instruction “add $r2, $r1, $r1” retired by ROB

## Slide 20
Single PRF to rename(7/7)
Source address access RAT and PRF get data and valid info
Destination address get a physical address from free_list replacing corresponding physical address in RAT, and put replaced physical address to release_list, and set corresponding “valid” to 0
When instruction execution finished, put data to PRF, and set destination physical address’s “valid” to 1
When instruction retired from ROB, put corresponding physical address from release_list to free_list

## Slide 21
Separate PRF to rename(1/6)

## Slide 22
Use two instructions to explain renaming process
add $r2, $r1, $r1
add $r30, $r1, $r2
Separate PRF to rename(2/6)

## Slide 23
Separate PRF to rename(3/6)
Rename after instruction “add $r2, $r1, $r1; add $r30, $r1, $r2”

## Slide 24
Separate PRF to rename(4/6)
State after instruction “add $r2, $r1, $r1” execution finished

## Slide 25
Separate PRF to rename(5/6)
State after instruction “add $r2, $r1, $r1” retired by ROB

## Slide 26
Separate PRF to rename(6/6)
Source address access RAT and ROB get data and valid info
Destination address set ARF “valid” to 0, and put dispatched rob_id to RAT as rename physical address
When instruction execution finished, put data to ROB, and set ROB “valid” to 1
When instruction retired from ROB, transfer data from ROB to ARF

## Slide 27
Simplified ROB rename(1/2)

## Slide 28
Simplified ROB rename(2/2)
Renaming process is same as separated PRF to rename
But don’t access ROB to get physical register value
Need ROB also broadcast it’s retire data to CDB (Common Data Bus)

## Slide 29: What other matter we need to deal?

## Slide 30
Speculative execution error
When speculative execution error occurs, RAT need restored to state just after branch instruction
Single PRF just need restore RAT, release_list and free_list by ROB remain slots
Separate PRF need restore RAT and ARF “valid” info by ROB remain slots

## Slide 31
If transfer operands to RS?
Single PRF can provide data access for execution unit, so data could hold in PRF or RS, depend on data width and execution unit number
Separate PRF must transfer data from ARF or PRF to RS

## Slide 32: Which method can we choose?

## Slide 33
Single PRF advantage
Don’t need carry data from one register to another
Effective use of every physical register, not like rob. Some instructions don’t update architecture register, but still occupy a rob data slot
Can enlarge ROB, but don’t increase physical address width
Can choose implement less physical register accordingly

## Slide 34
Separate PRF advantage
Hardware logic simple, especially simplified ROB rename
Less register file writing ports than single PRF to rename
Just need to access one level table to get desired data

## Slide 35: Bingo!!!

## Slide 36
A scheme----Single PRF

## Slide 37
Structure
64*64bits PRF, or less than 64 entries, 8w11r ports; dispatch operands to reserve station
32*6bit RAT
32*6bit free_list queue
Store release_list in ROB(size dependent ROB)
When execution error, restore RAT, by release_list in ROB